## Slide 1
Jiajun Wu, Yi Zhan, Zixuan Peng, Xinglong Ji, Guoyi Yu, Rong Zhao and Chao Wang
2021/02/24
Efficient Design of Spiking Neural Network with STDP Learning Based on Fast CORDIC

## Slide 2: Outline
Introduction
CORDIC in Spiking Neural Networks
Hardware Design and Implementation of Proposed Fast-convergence CORDIC SNN
Implementation Results and Discussion
Conclusion

## Slide 3: Introduction (1/5)
With the development of Internet-of-Thing (IoT), hardware accelerators with low latency and high energy-efficient become more and more important.
Face Recognition
Autonomous Driving
Object Tracking
Conventional artificial Neural Networks (ANN) are difficult to be implemented with on-line training due to the large amount of parameters and large network scales. Besides, the learning rule of ANN cannot reflect the learning strategy in human brains.

## Slide 4: Introduction (2/5)
Efficient design and implementation of bio-inspired neurons and synapses to enable on-line learning is very essential: performance, cost and power, etc.
Reduce latency.
Minimize power.
Ensure security.
Protect privacy.
It is a trend for AI accelerator
SNN on-line learning models – nonlinear dynamics [1]-[3]
Why on-line learning?
Intelligent IoT edge devices
STDP based and STDP-like (derived from STDP) synapse
Computation-intensive, hardware-expensive and power-hungry
especially for massive SNN design
LIF/Izhikevich neurons
Digital design
(selected)
Analog and Mixed
-signal design
More immune to device nonidealities and noises
Benefits from CMOS technology scaling
Very popular to massive hardware implementation
Causes
How to make a design choice for hardware implementation?

## Slide 5: Introduction (3/5)
In the recent research of digital SNN hardware, STDP-based synapses are implemented based on: (1) LUT; (2) Triangular approximation; (3) CORDIC.
(1) Look Up Tables (LUT)
(2) Triangular approximation
(3) CORDIC
CORDIC gained a lot of interests to implement neuron and synapse circuits
Use simple shift & add operations to approximate multiplication and exponentiation in a number of iterations => More accurate, less costly.

## Slide 6: Introduction (4/5)
Error analysis has also been performed to ensure the model-level accuracy of the proposed CORDIC neuron. However, there still has some cirical issues:
(1) The existing work has only assessed model-level precision and constructed a relatively simple network to demonstrate unsupervised Hebbian learning in terms of weight distribution;
(2) STDP learning speed has not been evaluated.
(3) The precision evaluation in the existing works has only analyzed the local spiking-train errors instead of network-level accuracy with respect to learning results.
In summary, hardware effieicny including learning performance and energy efficiency of CORDIC-based SNN design has not been sysmtematically studied.

## Slide 7: Introduction (5/5)
This study proposes a systematic design and evaluation method of CORDIC-based SNN, from theoretical CORDIC-level error analysis to application-level learning performance on MNIST dataset.
Design and evaluation flow of the
proposed CORDIC SNN
(1) Optimal CORDIC type and lowest bit-width precision can be identified, by trading affordable performance loss and hardware overhead for overall SNN hardware efficiency;
(2) A reconfigurable SNN design based on selected 8-bit fast-convergence CORDIC in [21] is presented;
(3) The FPGA results confirms that the propsoed SNN design outperformas the existing methods in terms of hardware efficiency, STDP-based learning performance and energy efficiency

## Slide 8: CORDIC in Spiking Neural Networks (1/4)
Network Model & Learning Rule
SNN architecture and working mechanism
Advantages:
High accuracy over MNIST dataset (95%)
Biological plausibility
Online learning -> On-chip learning
Including exponential calculations -> CORDIC

## Slide 9: CORDIC in Spiking Neural Networks (2/4)
Network Model & Learning Rule
With comparable classification accuracies (up to 95%), the selected STDP rule involves exponentiation, which is less complex than the other STDP variants based on power-law functions.
The exponentiation is implemented with CORDIC

## Slide 10: CORDIC in Spiking Neural Networks (3/4)
CORDIC for Exponentiation
Iteration No. of Conventional/Heidarpur’s CORDIC | 6 | 8 | 16 | 24
Average No. of Fast-convergence CORDIC | 2.27 | 4.18 | 7.88 | 10.48
Saving of Redundant Iterations | 62.2% | 47.8% | 50.8% | 56.3%
Illustration of CORDIC algorithms (a) conventional CORDIC, (b) fast-convergence CORDIC
Average number of iterations

## Slide 11: CORDIC in Spiking Neural Networks (4/4)
Performance Analysis of CORDIC SNN
Classification accuracy of SNN based on different CORDIC under various bit-width precision.
6 and 8-bit are selected

## Slide 12: Hardware Design and Implementation (1/3)
Removing Inhibitory Neurons for simplification
Proposed SNN architecture by substituting inhibitory neurons in original model with intra-layer inhibitory synapses
Accuracy loss is acceptable!
Intra-layer inhibitory synapses among the excitatory neurons is proposed to optimize the SNN architecture to reduce hardware complexity and energy consumption by removing the inhibitory neurons

## Slide 13: Hardware Design and Implementation (2/3)
Synaptic Circuit Design and Dataflow
The target traces are shared between different synapses
Local weight update (local learning)

## Slide 14: Hardware Design and Implementation (3/3)
System Design and Dataflow
System design
Time-Division Multiplexing

## Slide 15: Implementation Results and Discussion (1/3)
HARDWARE UTILIZATION AND MAX SPEED FOR SNN WITH DIFFERENT IMPLEMENTATIONS
Requiring extra LUT to store scaling factors and logic slices to perform shift & add based scaling.
Heidarpur’s CORDIC requires more shift & add operations to multiply the pre-calculated values in the iterations, causing a much longer carry chain than the other CORDIC designs (lower frequency).

## Slide 16: Implementation Results and Discussion (2/3)
Energy Efficiency Evaluation
For fair comparison, the energy consumption must be divided into “energy per synaptic operation (SOP)”
As the fast-convergence CORDIC takes much fewer iterations and computation to finish STDP calculation, the proposed fast-convergence CORDIC SNN design achieves dynamic energy saving significantly.

## Slide 17: Implementation Results and Discussion (3/3)
Other Evaluations
Acceleration
Energy per image

## Slide 18: Conclusion
A system design and evaluation method of CORDIC SNN is proposed to evaluate the hardware efficiency of SNN based on different CORDIC algorithm types and bit-width precisions. The comprehensive evaluation proves that selected 8-bit fast-convergence CORDIC with pipeline AR method outperforms both the conventional and the state-of-the-art CORDIC designs, in terms of the theoretical CORDIC-level error analysis, the application-level learning and classification performance on MNIST benchmark.
The implementation results confirm that the proposed fast-convergence CORDIC SNN design has better hardware efficiency than the conventional and state-of-the-art CORDIC methods, in terms of the STDP learning speed and energy efficiency, the image processing speed and learning convergence speed.